First switch ON the CN, gNB, and UE

iperf -s -u -i 1 -B 10.0.0.2 #run on UE as a server in T1

sudo docker exec -it oai-upf bash # for UPF root path in T2

sudo docker exec -it oai-ext-dn bash # for ext-server root path in T3

sudo docker exec -it oai-upf iperf -s -u -i 1 -B 192.168.70.134 # run on UPF as a server in T2 as in a home

sudo docker exec -it oai-ext-dn iperf -c 192.168.70.134 -u -b 300K -t 10 -i 1 #run on AS as a client in T4

# code for congestion either server or client
#if u r running server as UPF and client as a EXT-DN =====It is Downlink (then congestion run should be on server only) in T2

sudo tc qdisc add dev eth0 root netem rate 80Kbit

sudo tc qdisc add dev eth0 root tbf rate 300Kbit burst 32kbit latency 400ms

sudo tc qdisc add dev eth0 root netem delay 100ms loss 5% rate 300Kbit

# 1. Add TBF to control rate
sudo tc qdisc add dev eth0 root handle 1: tbf rate 300Kbit burst 38kbit latency 400ms

# 2. Add NetEm to inject packet loss
sudo tc qdisc add dev eth0 parent 1:1 handle 10: netem loss 10%

check the congestion

tc qdisc show dev eth0

delete the congestion

sudo tc qdisc del dev eth0 root

UPF as a server
iperf -s -u -i 1 -B 192.168.70.134 #UPF IP Address

Application server is Client
iperf -c 192.168.70.134 -u -b 300K -t 100 i 1 # ext-server

Note: we need to run client side congestion then u will get fluctuation congestion effect from server side

For Multi UE
https://gitlab.eurecom.fr/oai/openairinterface5g/-/blob/develop/doc/NR_SA_Tutorial_OAI_multi_UE.md

Steps to run the Integration of IBN_ZTN:
1. Run the Congestion_gen_UPF_AS.py file to generate the congestion of 300 values between UPF and AS.
2. Run e2e_bandwidth_measurement_after_congestion.py and use “poisson_distribution_with_drift_value_300(11).csv” like this for different files we have to call to measure the e2e performance of the network. This will generate e2ebandwidth .csv file of 300 values for the given .csv file. By this way, we generated 2000 BW values.
3. create the BiLSTM model file (.h5) using 2000 BW values.run this code Bilstm_gen_oaicong_data.py
4. Then, run final_integration1.py, to get the “E2E throughput achieved applying ZTN closed loop to meet ID user intent of 300 kbps” and 450 kbps figures. This will use the 15th and 39th episode files to for find the optimal and sub-optimal solution and graph.
5. Finally, run the calculate_average_40_episodes.py code to calculate the average value of each episodes which takes the each episode .csv files from the previous step.
Note in a Terminal:
For OOD case, run the sudo docker exec -it oai-ext-dn iperf -c 10.0.0.2 -u -b 500K -t 10000 -i 1
For ID case, run the sudo docker exec -it oai-ext-dn iperf -c 10.0.0.2 -u -b 300K -t 10000 -i 1

6. run the Compari_monte_testbed_ID_OOD.py file to get the comparision graph of ID and OOD case.